## Slide 1: PL-4000T Feature – Version Tracking
December 2025

## Slide 2: Change log
Rev 1.0 11 December 2025 – Initial release version

## Slide 3: Front Panel View
4x Uplink Ports:
  Uplink 1-4 : 4xCFP2-DCO or 4xQSFPDD-DCO
  A mixture of uplink module types is not allowed
  Using System mode user control if Acacia or Fujitsu uplinks (will affect GCC and encryption)
16x Client Ports:
  L1-L16: 100G QSFP28
  L4,L8,L12,L16: optional 400G QSFP-DD
MUX/DEMUX 4:1 Port:
  MPO: Gathers 4x Uplinks + OSC
2x LC Ports:
  When no OSC is installed, the COM is connected to line
  When OSW is installed, COM/1 & COM2 shall be connected to Line
Management ports
  2x SFP: MNG1 and MNG2
  2x RJ45 for LAN1, LAN2
  RJ45 for CLI - local Management
  RJ45 for External Alarms

## Slide 4: Interoperability with other devices
PL-4000T can be Interoperability with the following devices:
  PL-4000G
  PL-2000T (need to be verified)
Uplink modes need to be the same in both devices

## Slide 5: PL-4000G – PL-4000T Interoperability
 |  |  |  |  | PL-4000G QSFPDD | 
 | Uplink | Service type | modulation | client | 100G | 400G
PL4000T | QSFPDD | 400G OpenZR+ | 16QAM | 100G | Traffic run | NA
 |  | 300G OpenZR+ | 8QAM |  | Traffic run | 
 |  | 200G OpenZR+ | 8QAM |  | Traffic run | 
 |  | 200G OpenZR+ | QPSK |  | Traffic run | 
 |  | 400G OpenROADM | 16QAM |  | Traffic run | 
 |  | 300G OpenROADM | 8QAM |  | Traffic run | 
 |  | 200G OpenROADM | 8QAM |  | Traffic run | 
 |  | 200G OpenROADM | QPSK |  | Traffic run | 
 | CFP2 | 400G OpenZR+ | 16QAM |  | Traffic run | 
 |  | 300G OpenZR+ | 8QAM |  | Traffic run | 
 |  | 200G OpenZR+ | 8QAM |  | Traffic run | 
 |  | 200G OpenZR+ | QPSK |  | Traffic run | 
 |  | 400G OpenROADM | 16QAM |  | Traffic run | 
 |  | 300G OpenROADM | 8QAM |  | Traffic run | 
 |  | 200G OpenROADM | 8QAM |  | Traffic run | 
 |  | 200G OpenROADM | QPSK |  | Traffic run | 
 | QSFPDD | 400G OIF ZR | 16QAM | 400G | NA | Traffic run
 |  | 400G OpenZR+ | 16QAM |  |  | Traffic run
 |  | 400G OpenROADM | 16QAM |  |  | Traffic run
 | CFP2 | 400G OpenZR+ | 16QAM |  |  | Traffic run
 |  | 400G OpenROADM | 16QAM |  |  | Traffic run

## Slide 6: GA - Version 2.2.22

## Slide 7: Uplink supported 1/3
Uplink Type | Uplink modes | PM Supported | Alpha test | Comment
ACACIA CFP2 (M30/M35) | OpenROADM: ▪ 200G OpenROADM 8QAM QPSK ▪ 300G OpenROADM ▪ 400G OpenROADM | OpenROADM: OTU Section OTU Far Section ODU Section ODU Far Section FEC Corrected FEC Uncorrected FEC Error Ratio Optical PM | V | 200G Open ROADM with Bugs
 | • OpenZR+: ▪ 200G OpenZR+ 8QAM QPSK ▪ 300G OpenZR+ ▪ 400G OpenZR+ | OpenZR+: CRC Errors FEC Corrected FEC Uncorrected FEC Error Ratio Optical PM |  | 

## Slide 8: Uplink supported 2/3
Uplink Type | Uplink modes | PM Supported | Alpha test | Comment
Fujitsu CFP2 | OpenROADM: ▪ 200G OpenROADM 16QAM 8QAM QPSK ▪ 300G OpenROADM ▪ 400G OpenROADM | • OpenROADM: OTU Section OTU Far Section ODU Section ODU Far Section FEC Corrected FEC Uncorrected FEC Error Ratio Optical PM | V | W/O Encryption Mix of Services: 4x100Gbe 3x100Gbe+1xOTU4 2x100Gbe+2xOTU4 4xOTU4 1x400Gbe
 | • OpenZR+: ▪ 200G OpenZR+ 16QAM 8QAM QPSK ▪ 300G OpenZR+ ▪ 400G OpenZR+ | • OpenZR+: CRC Errors FEC Uncorrected Optical PM |  | 
ACACIA QSFPDD-DCO (E20/E25) 4104 | 400G ZR – 16QAM | FEC Uncorrected Optical PM | V | 

## Slide 9: Uplink supported 3/3
Uplink Type | Uplink modes | PM Supported | Alpha test | Comment
ACACIA QSFPDD-DCO (HK9) | Open ZR: ▪ 400G ZR | • Open ZR: CRC Errors FEC Corrected FEC Uncorrected FEC Error Ratio Optical PM | V | W/O Encryption
 | OpenROADM: ▪ 200G OpenROADM 16QAM 8QAM QPSK ▪ 300G OpenROADM ▪ 400G OpenROADM | • OpenROADM: OTU Section OTU Far Section ODU Section ODU Far Section FEC Uncorrected Optical PM |  | 
 | • OpenZR+: ▪ 200G OpenZR+ 16QAM 8QAM QPSK ▪ 300G OpenZR+ ▪ 400G OpenZR+ | • OpenZR+: CRC Errors FEC Uncorrected Optical PM |  | 

## Slide 10: Client supported
Client Signal | Form Factor | PMD | Connector | Alpha | comment
400G | QSFPDD | LR8 | Duplex LC |  | 
400G | QSFPDD | FR8 | Duplex LC |  | 
400G | QSFPDD | SR8 | MPO16 |  | 
400G | QSFPDD | DR4 | MPO12 |  | 
400G | QSFPDD | FR4 | Duplex LC |  | 
400G | QSFPDD | LR4 | Duplex LC |  | 
4x100G | QSFPDD | DR4 | MPO12 with Breakout to 4x100G |  | 
4x100G | QSFPDD | DR4+ | MPO12 with Breakout to 4x100G |  | 
4x100G | QSFPDD | 4x100LR | MPO12 with Breakout to 4x100G |  | 
100G | QSFP28 |  | Duplex LC |  | 
OTU4 | QSFP28 |  | Duplex LC |  | 

## Slide 11: Feature added
Upgrade OpenSSL and OS version
2 System Mode PLN-A/ PLN-F
Radius – Exit on Reject mode
TCA
NTP
Syslog TLS
System high/low temperature alarms
DMP
Multi Chassis - removed
Topology button removed - keeps only local links in MIB

## Slide 12: Version 2.3.x

## Slide 13: Uplink supported 1/3
Uplink Type | Uplink modes | PM Supported | Alpha test | Comment
ACACIA CFP2 (M30/M35) | OpenROADM: ▪ 200G OpenROADM 8QAM QPSK ▪ 300G OpenROADM ▪ 400G OpenROADM | OpenROADM: OTU Section OTU Far Section ODU Section ODU Far Section FEC Corrected FEC Uncorrected FEC Error Ratio Optical PM | V | 200G Open ROADM with Bugs
 | • OpenZR+: ▪ 200G OpenZR+ 8QAM QPSK ▪ 300G OpenZR+ ▪ 400G OpenZR+ | OpenZR+: CRC Errors FEC Corrected FEC Uncorrected FEC Error Ratio Optical PM |  | 

## Slide 14: Uplink supported 2/3
Uplink Type | Uplink modes | PM Supported | Alpha test | Comment
Fujitsu CFP2 | OpenROADM: ▪ 200G OpenROADM 16QAM 8QAM QPSK ▪ 300G OpenROADM ▪ 400G OpenROADM | • OpenROADM: OTU Section OTU Far Section ODU Section ODU Far Section FEC Corrected FEC Uncorrected FEC Error Ratio Optical PM | V | With Encryption Mix of Services: 4x100Gbe 3x100Gbe+1xOTU4 2x100Gbe+2xOTU4 4xOTU4 1x400Gbe
 | • OpenZR+: ▪ 200G OpenZR+ 16QAM 8QAM QPSK ▪ 300G OpenZR+ ▪ 400G OpenZR+ | • OpenZR+: CRC Errors FEC Uncorrected Optical PM |  | 
ACACIA QSFPDD-DCO (E20/E25) 4104 | 400G ZR – 16QAM | FEC Uncorrected Optical PM | V | 

## Slide 15: Uplink supported 3/3
Uplink Type | Uplink modes | PM Supported | Alpha test | Comment
ACACIA QSFPDD-DCO (HK9) | Open ZR: ▪ 400G ZR | • Open ZR: CRC Errors FEC Corrected FEC Uncorrected FEC Error Ratio Optical PM | V | With Encryption
 | OpenROADM: ▪ 200G OpenROADM 16QAM 8QAM QPSK ▪ 300G OpenROADM ▪ 400G OpenROADM | • OpenROADM: OTU Section OTU Far Section ODU Section ODU Far Section FEC Uncorrected Optical PM |  | 
 | • OpenZR+: ▪ 200G OpenZR+ 16QAM 8QAM QPSK ▪ 300G OpenZR+ ▪ 400G OpenZR+ | • OpenZR+: CRC Errors FEC Uncorrected Optical PM |  | 

## Slide 16: Uplink supported 3/3
Uplink Type | Uplink modes | PM Supported | Alpha test | Comment
ACACIA 400G QSFPDD-ULH | ULH: ▪ 400G ULH 75GHz ▪ 400G ULH 100GHz ▪ 400G ULH 150GHz | FEC Uncorrected Optical PM |  | 
Fujitsu 400G DD-DCO OpenZR - 4105S | 400G ZR – 16QAM | FEC Uncorrected Optical PM |  | 

## Slide 17: Client supported
Client Signal | Form Factor | PMD | Connector | Alpha | comment
400G | QSFPDD | LR8 | Duplex LC |  | 
400G | QSFPDD | FR8 | Duplex LC |  | 
400G | QSFPDD | SR8 | MPO16 |  | 
400G | QSFPDD | DR4 | MPO12 |  | 
400G | QSFPDD | FR4 | Duplex LC |  | 
400G | QSFPDD | LR4 | Duplex LC |  | 
4x100G | QSFPDD | DR4 | MPO12 with Breakout to 4x100G |  | 
4x100G | QSFPDD | DR4+ | MPO12 with Breakout to 4x100G |  | 
4x100G | QSFPDD | 4x100LR | MPO12 with Breakout to 4x100G |  | 
4x100G | QSFPDD | 4x100FR | Duplex LC |  | Regeneration
100G | QSFP28 |  | Duplex LC |  | 
OTU4 | QSFP28 |  | Duplex LC |  | 
100/400 DAC |  |  | DAC | need to be verified | 

## Slide 18: Feature supported
Radius NAS identifier
CLI improvement – inventory, SNMP, XPDR, etc.
Optical switch- switching above 50mSec (takes more than 2 sec) – Fixed
Mix of Acacia and Fujitsu on the same product (GCC/ encryption according to system mode)

## Slide 19: Future Version 2.4.x / 3.1.x

## Slide 20: Feature supported